## Slide 1: Memory Elements Engineering 304
Latches and Flip-Flops
Registers
  VHDL versions
Shift Registers and Counters
  VHDL versions

## Slide 2: Cross-Coupled NOR Latch
Simplest form of memory
Avoid invalid state
(Q-bar=Q)
Q
R
S
Q
__

## Slide 3: Gated Latch
Cross-Coupled NAND need S and R inverted
Often SR latches include a control line (Enable)
S
R
En
Q
Q

## Slide 4: Level vs. Edge
Latches are level-sensitive using Enable input (Qa)
  book calls the Enable the “CLK”
Flip-flops are edge-triggered using Clock input
  Rising (Qb) or Falling (Qc)

## Slide 5: Level vs. Edge
Latches are level-sensitive using Enable input (Qa)
  book calls the Enable the “CLK”
Flip-flops are edge-triggered using Clock input
  Rising (Qb) or Falling (Qc)

## Slide 6: Level vs. Edge
Latches are level-sensitive using Enable input (Qa)
  book calls the Enable the “CLK”
Flip-flops are edge-triggered using Clock input
  Rising (Qb) or Falling (Qc)

## Slide 7: Level vs. Edge
Latches are level-sensitive using Enable input (Qa)
  book calls the Enable the “CLK”
Flip-flops are edge-triggered using Clock input
  Rising (Qb) or Falling (Qc)

## Slide 8: Characteristic Table
Truth Table that includes time aspect (Q(t) -> Q(t+1))
    Given certain inputs, what output is expected from the memory device?
  SR
  D
  T
  JK
An “Excitation Table” lists the required inputs needed to cause a particular output change

## Slide 9: Characteristic Tables

## Slide 10: Characteristic Tables

## Slide 11: Excitation Tables

## Slide 12: Excitation Tables

## Slide 13: VHDL D Flip-Flop
ENTITY flipflop IS
PORT ( D, Resetn, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
END flipflop ;
ARCHITECTURE Behavior OF flipflop IS
BEGIN
PROCESS ( ______________)
BEGIN
IF Resetn = '0' THEN
Q <= '0' ;
ELSIF Clock'EVENT AND Clock = '1' THEN
Q <= D ; -- notice there is no “Else” clause
END IF ;
END PROCESS ;
END Behavior ;

## Slide 14: VHDL D Flip-Flop
ENTITY flipflop IS
PORT ( D, Resetn, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
END flipflop ;
ARCHITECTURE Behavior OF flipflop IS
BEGIN
PROCESS ( Resetn, Clock )
BEGIN
IF Resetn = '0' THEN
Q <= '0' ;
ELSIF Clock'EVENT AND Clock = '1' THEN
Q <= D ; -- notice there is no “Else” clause
END IF ;
END PROCESS ;
END Behavior ;
Sens. List must be exactly this!
If-elsif must be exactly this!

## Slide 15
VHDL n-Bit Register
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY regn IS
GENERIC ( N : INTEGER := 16 ) ;
PORT ( D : IN STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
Resetn, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
END regn ;
ARCHITECTURE Behavior OF regn IS
BEGIN
PROCESS ( ____________________)
BEGIN
IF Resetn = '0' THEN
Q <= (OTHERS => '0') ;
ELSIF ____________________________ THEN
Q <= D ;
END IF ;
END PROCESS ;
END Behavior ;

## Slide 16
VHDL n-Bit Register
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY regn IS
GENERIC ( N : INTEGER := 16 ) ;
PORT ( D : IN STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
Resetn, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
END regn ;
ARCHITECTURE Behavior OF regn IS
BEGIN
PROCESS ( Resetn, Clock )
BEGIN
IF Resetn = '0' THEN
Q <= (OTHERS => '0') ;
ELSIF Clock'EVENT AND Clock = '1' THEN
Q <= D ;
END IF ;
END PROCESS ;
END Behavior ;

## Slide 17: Flip-Flop Test Bench
Device Under Test (DUT)
Test Bench
Inputs
Outputs
Inputs
Outputs

## Slide 18
Test Bench Code
ENTITY flipflop_TestBench IS
END flipflop_TestBench;
ARCHITECTURE test OF flipflop_TestBench IS
component flipflop IS port ( -- declare the component
D, Resetn, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
end component flipflop ;
signal Dsig : std_logic; -- declare the internal signals
signal Resetnsig : std_logic;
signal Clocksig : std_logic;
signal Qsig : std_logic;
BEGIN
DUT: flipflop port map ( -- instantiate the flipflop
D => Dsig, Resetn => Resetnsig, Clock => Clocksig, Q => Qsig
);

## Slide 19
Test Bench Code (cont.)
process is -- no sensitivity list => use “wait” instead
begin
Resetnsig <= '0';
Clocksig <= '0';
Dsig <= '1';
wait for 10 ns; -- reset everything
assert Qsig = '0' report "Q not reset to zero"
severity WARNING;
Resetn <= '1';
wait for 10 ns; -- reset off, but still Q=0
assert Qsig = '0' report "Q not staying at zero after reset"
severity WARNING;
Clocksig <= '1'; -- rising edge should clock in D=1
wait for 10 ns; -- let clock edge do something
assert Qsig = '1' report "Q should now be 1"
severity WARNING;

## Slide 20
Test Bench Code (cont.)
Dsig <= '0';
wait for 10 ns; -- should be no change when changing D
assert Qsig = '1' report "Q not staying as 1"
severity WARNING;
Clocksig <= '0';
wait for 10 ns; -- should be no change with falling clk
assert Qsig = '1' report “Q changed on falling clock"
severity WARNING;
Clocksig <= '1'; -- rising edge
wait for 10 ns; -- D=0 should be clocked in
assert Qsig = '0' report “D=0 not clocked in"
severity WARNING;
wait; -- never go past this spot – infinite loop-like
end process;
END test;

## Slide 21: Sequential Devices
Registers
  Shift
  Parallel In, Serial Out
Counters
  Up, down, up/down, modulo-n
  Ring, Johnson (also shift registers)

## Slide 22: Shift Register Example

## Slide 23: Asynchronous Counter
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
Flip-flops are always set to toggle – must control the clock

## Slide 24: Synchronous Counter
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
T
Q
Q
Q
3
Always clocked – must control toggling with proper flip-flop inputs -> preferred design!

## Slide 25: Modulo-n Counters
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
As soon as count(Q2 Q1 Q0) = ________________then asynchronously clear flip-flops.
    (5 is never really seen by the user)

## Slide 26: Modulo-n Counters
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
- As soon as count(Q2 Q1 Q0) = “1d1” = 5 (or 7), then asynchronously clear flip-flops. (5 is never really seen by the user)
- Also, consider the 001 to 010 transition

## Slide 27: Modulo-n Counter
Asynchronous load or clear
  Check for trouble with bits changing slightly out of order
Best practice is to only use asynchronous clearing through the global chip reset

## Slide 28
VHDL Enabled Counter
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
USE ieee.std_logic_unsigned.all ;
ENTITY upcount IS
PORT ( Clock, Resetn, E : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR (3 DOWNTO 0)) ;
END upcount ;
ARCHITECTURE Behavior OF upcount IS
SIGNAL Count : STD_LOGIC_VECTOR (3 DOWNTO 0) ;
BEGIN
PROCESS ( Clock, Resetn )
BEGIN
IF Resetn = '0' THEN Count <= "0000" ;
ELSIF (Clock'EVENT AND Clock = '1') THEN
IF E = '1' THEN Count <= Count + 1 ;
ELSE Count <= Count ;
END IF ;
END IF ;
END PROCESS ;
Q <= Count ; -- finally, assign the output Q from the signal Count
END Behavior ;

## Slide 29
VHDL Enabled Counter
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
USE ieee.std_logic_unsigned.all ;
ENTITY upcount IS
PORT ( Clock, Resetn, E : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR (3 DOWNTO 0)) ;
END upcount ;
ARCHITECTURE Behavior OF upcount IS
SIGNAL Count : STD_LOGIC_VECTOR (3 DOWNTO 0) ;
BEGIN
PROCESS ( Clock, Resetn )
BEGIN
IF Resetn = '0' THEN Count <= "0000" ;
ELSIF (Clock'EVENT AND Clock = '1') THEN
IF E = '1' THEN Count <= Count + 1 ;
-- ELSE Count <= Count ; -- not needed as assumed
END IF ;
END IF ;
END PROCESS ;
Q <= Count ; -- finally, assign the output Q from the signal Count
END Behavior ;

## Slide 30
VHDL Modulo-n Counter

## Slide 31
VHDL Enabled Counter
ARCHITECTURE Behavior OF counter IS
component counter_ex is
generic(NUM_BITS : integer := 4; MIN_CNT : integer := 4;
MAX_CNT : integer := 13);
port(CLK, RSTn : IN std_logic;
Count : OUT std_logic_vector((NUM_BITS – 1 downto 0));
end component counter_ex;
BEGIN
C0 : component counter_ex
generic map (NUM_BITS => 4, MIN_CNT => 2, MAX_CNT => 11)
port map (CLK => my_clock, RSTn => my_reset, Count => Count0);
C1 : component counter_ex
generic map (NUM_BITS => 6, MIN_CNT => 3, MAX_CNT => 49)
port map (CLK => my_clock, RSTn => my_reset, Count => Count1);
C2 : component counter_ex
generic map (NUM_BITS => 3, MIN_CNT => 1, MAX_CNT => 7)
port map (CLK => my_clock, RSTn => my_reset, Count => Count2);
END Behavior ;

## Slide 32
VHDL Modulo-n Counter - Quartus