## Slide 1: ENGR-304-L
Software Lab 03

## Slide 2: Agenda
Attendance
Recap
Functions & Recursion
Functions in Assembly
The Stack
Getting Started

## Slide 3: Recap
Assembly programming language is closely related to machine code
NIOS CPU executes machine code while running program
Program results can be found in registers or memory
Compiler optimization can be a useful tool

## Slide 4: Functions
Functions defined by behavior, inputs, & outputs
Function
Behavior
Function
Inputs
Function
Outputs

## Slide 5: Functions
Functions defined by behavior, inputs, & outputs
Often referred to as definition, parameters, return values
Function
Definition
Function
Parameters
Function
Return Values

## Slide 6: Recursion
Recursive problems can be divided into sub-problems
The recursive solution is identical for the original problem and the sub-problems
There must be at least 1 base-case defining a “smallest” sub-problem with a non-recursive solution
Ex: Fibonacci
Fibonacci(n) = Fibonacci(n-1) + Fibonacci(n-2) // n > 1
Fibonacci(n) = n // 0 <= n <= 1

## Slide 7: Recursion
Fib(n) = Fib(n-1) + Fib(n-2) // n > 1
Fib(n) = n // 0 <= n <= 1
Problem is solved by sub-problems

## Slide 8: Recursion
Fib(n) = Fib(n-1) + Fib(n-2) // n > 1
Fib(n) = n // 0 <= n <= 1
Problem is solved by sub-problems
There are 2 base-cases

## Slide 9: Recursion
Fib(n) = Fib(n-1) + Fib(n-2) // n > 1
Fib(n) = n // 0 <= n <= 1
Problem is solved by sub-problems
There are 2 base-cases
https://www8.cs.umu.se/kurser/TDBA77/VT06/algorithms/BOOK/BOOK25/IMG313.GIF

## Slide 10: Recursive Functions
Function Definition
Recursive functions call themselves as sub-problems
Function
Definition
(same as outer)
Inner Function
Parameters
(if not base-case)
Inner Function
Return Values
Outer Function
Parameters
Outer Function
Return Values
Check For Base-Case
Base-Case Return Values
(if base-case)

## Slide 11: Recursive Functions
C Function Declarations
Return type
Function name
Parameter list
First parameter type
First parameter name

## Slide 12: Recursive Functions
C Function Definitions
Local variables
Recursive function calls
Return statement
Recursive base-case check

## Slide 13: Assembly Functions
Global label for
function name
“call”
“ret”

## Slide 14: NIOS Function Registers
Standard register usage “agreement”
R2, R3 – return value
R4, R5, R6, R7 – parameters
RA (R31) – return address
Callee-saved vs Caller-saved

## Slide 15: The Stack
Stacks & Queues
Ex: buffet dishes & amusement park lines
https://cdn-images-1.medium.com/max/523/1*asgh4mx9ez5Ji8PmBayS8g.png

## Slide 16: The Stack
Stacks & Queues
Ex: buffet dishes & amusement park lines
Stack Push & Pop
https://cdn-images-1.medium.com/max/523/1*asgh4mx9ez5Ji8PmBayS8g.png
Push
Pop

## Slide 17: The Stack
Stack is useful for nested function calls (ex: recursion)
https://cdn-images-1.medium.com/max/523/1*asgh4mx9ez5Ji8PmBayS8g.png
Info about 1st function call
Push

## Slide 18: The Stack
Stack is useful for nested function calls (ex: recursion)
https://cdn-images-1.medium.com/max/523/1*asgh4mx9ez5Ji8PmBayS8g.png
Info about 1st function call
Info about 2nd function call
Push

## Slide 19: The Stack
Stack is useful for nested function calls (ex: recursion)
https://cdn-images-1.medium.com/max/523/1*asgh4mx9ez5Ji8PmBayS8g.png
Info about 1st function call
Info about 2nd function call
Info about 3rd function call
Info about 4th function call
Info about 5th function call
Push x3

## Slide 20: The Stack
Stack is useful for nested function calls (ex: recursion)
https://cdn-images-1.medium.com/max/523/1*asgh4mx9ez5Ji8PmBayS8g.png
Info about 1st function call
Info about 2nd function call
Info about 3rd function call
Info about 4th function call
Pop

## Slide 21: The Stack
Stack is useful for nested function calls (ex: recursion)
https://cdn-images-1.medium.com/max/523/1*asgh4mx9ez5Ji8PmBayS8g.png
Info about 1st function call
Info about 2nd function call
Info about 3rd function call
Pop

## Slide 22: The Stack
Stack is useful for nested function calls (ex: recursion)
https://cdn-images-1.medium.com/max/523/1*asgh4mx9ez5Ji8PmBayS8g.png
Pop x3
<empty>

## Slide 23: The Stack
“Info about Xth function call”  preserve state
Even though recursive calls use the
same n parameter and return statement,
the former call should not have its n
changed by the sub-call. We need to
preserve state.

## Slide 24: The Stack
“Info about Xth function call”  preserve state
https://cdn-images-1.medium.com/max/523/1*asgh4mx9ez5Ji8PmBayS8g.png
State of registers as used by 1st function call
State of registers as used by 2nd function call
State of registers as used by 3rd function call

## Slide 25: The Stack
“Info about Xth function call”  preserve state
https://cdn-images-1.medium.com/max/523/1*asgh4mx9ez5Ji8PmBayS8g.png
State of registers as used by 1st function call
State of registers as used by 2nd function call
State of registers as used by 3rd function call
Since the stack is in memory,
Push is done by “stw” = add to the top of the stack
Pop is done by “ldw” = remove from the top of the stack

## Slide 26: The Stack
“Info about Xth function call”  preserve state
https://cdn-images-1.medium.com/max/523/1*asgh4mx9ez5Ji8PmBayS8g.png
R# as used by 1st function call
R# as used by 1st function call
R# as used by 2nd unction call
Since the stack is in memory,
Push is done by “stw” = add to the top of the stack
Pop is done by “ldw” = remove from the top of the stack
The registers all share the same stack, may be several for
each function call (arbitrarily showing 2 for 1st and 1 for 2nd)

## Slide 27: The Stack
“Info about Xth function call”  preserve state
https://cdn-images-1.medium.com/max/523/1*asgh4mx9ez5Ji8PmBayS8g.png
State of a register on stack
State of a register on stack
State of a register on stack
Since the stack is in memory,
Push is done by “stw” = add to the top of the stack
Pop is done by “ldw” = remove from the top of the stack
R27 (sp) is the stack pointer, it points to the top of the stack
(1 byte beyond the last used memory address)
sp
Start of last
used block
Base of
stack

## Slide 28: The Stack
Pushing onto stack, note sp decremented
because stack memory goes from end to
start (stack & heap work towards each other)
Note: comments removed for slides, always use good comments in assembly, portions of function are redacted
Popping from stack, note sp has same value
in the end as it did originally
These calls continue to use and change the stack,
but each pops it back to the state it was in
originally before returning so the caller doesn’t
notice the changes (state preserved)

## Slide 29: Lab SW03 Tips
Use only the n=0 recursive base case for Factorial program
Use optimization level –O1
Refer to the NIOS summary reference “registers table”
Refer to “NIOS Processor Stack” slide deck for details on assembly functions & stack usage

## Slide 30: Getting Started
Setup project directory for SW03 on the H: drive
Download SW03 files from Moodle or S: drive
Also locate the reference files from SW01 & SW02
Start following directions in the lab assignment document

## Slide 31: Reference Diagrams
The remaining slides explain certain file types and compilation processes that will apply throughout the semester

## Slide 32
Windows 10 PC
Altera DM
Software (Loading/Debugging)
Altera DE2 Board
Quartus
FGPA
NIOS Processor Image
(Flashed)
Software (Executing)
NIOS Processor Image
NIOS Processor Image
Peripheral Devices
(Ex: switches, buttons, hex displays)
Switches
Timer
7Seg Displays
LEDs
Keys

## Slide 33
Compiler-Generated for NIOS: view in debugger, depends on optimization
Assembly Code
We are using these in Engr304 Lab
Altera DE2 FPGA Hardware
A system configuration for this FPGA component has been generated, it executes our program and can be viewed by the debugger
NIOS Processor Image
Compiler-Generated for NIOS: view in memory, determine from reference
Machine Code
“portable” C-Code
C Code
Compiling
Assembling
Loading
We don’t have these in Engr304 Lab
NIOS Processor Hardware
Loading
Flashed

## Slide 34
Assembly code is fairly platform-specific and may be shared by families of processors. Assembly code is almost at the level of machine code, but is more readable and maintainable than raw 0’s and 1’s. It is assembled into machine code.
Assembly Code
An FPGA is like “general purpose hardware” which can be flashed with an image of a certain circuit. In this case, the FPGA is flashed with the NIOS Processor Image which allows it to perform essentially like a dedicated NIOS Processor hardware device.
Altera DE2 FPGA Hardware
Machine code can be loaded onto an image of the processor for which it was assembled and executed therein. In this case, the processor image is the same as a physical processor (for the most part).
NIOS Processor Image
Machine code is the raw 0’s and 1’s that can be interpreted by the processor in order to execute programs. It is rarely used or modified directly since changes to source code occur at the C Code or Assembly Code levels instead. However, it may be captured as an artifact of the build process for a particular program.
Machine Code
C Code is fairly platform-agnostic and can be run on a variety of difference processors, each with their own assembly instruction sets. C Code is compiled into assembly code which is beneficial because the combination of C Code and a compiler has better maintainability, portability, readability, and shorter development times than raw assembly code.
C Code
Compiling
Assembling
Loading
Machine code can be loaded onto the processor for which it was assembled and “physically” executed therein.
NIOS Processor Hardware
Loading
Flashed

## Slide 35
Assembly Code
An FPGA is like “general purpose hardware” which can be flashed with an image of a certain circuit. In this case, the FPGA is flashed with the NIOS Processor Image which allows it to perform essentially like a dedicated NIOS Processor hardware device.
Altera DE2 FPGA Hardware
Machine code can be loaded onto an image of the processor for which it was assembled and executed therein. In this case, the processor image is the same as a physical processor (for the most part).
NIOS Processor Image
Machine Code
C Code
Compiling
Assembling
Loading
NIOS Processor Hardware
Loading
Flashed
In Lab, the QSys setup helps configure and define what the NIOS Processor Image is.

## Slide 36
Assembly Code
An FPGA is like “general purpose hardware” which can be flashed with an image of a certain circuit. In this case, the FPGA is flashed with the NIOS Processor Image which allows it to perform essentially like a dedicated NIOS Processor hardware device.
Altera DE2 FPGA Hardware
Machine code can be loaded onto an image of the processor for which it was assembled and executed therein. In this case, the processor image is the same as a physical processor (for the most part).
NIOS Processor Image
Machine Code
C Code
Compiling
Assembling
Loading
NIOS Processor Hardware
Loading
Flashed
In Lab, the Altera DE2 boards are FPGA’s (+ some peripherals) that we load the image onto.

## Slide 37
Assembly Code
An FPGA is like “general purpose hardware” which can be flashed with an image of a certain circuit. In this case, the FPGA is flashed with the NIOS Processor Image which allows it to perform essentially like a dedicated NIOS Processor hardware device.
Altera DE2 FPGA Hardware
Machine code can be loaded onto an image of the processor for which it was assembled and executed therein. In this case, the processor image is the same as a physical processor (for the most part).
NIOS Processor Image
Machine Code
C Code
Compiling
Assembling
Loading
NIOS Processor Hardware
Loading
Flashed
In Lab, part of flashing the FPGA involves compiling a .sof file from a .bdf file. The .bdf holds the NIOS component from QSys and the .sof is specific to the DE2.

## Slide 38
Assembly code is fairly platform-specific and may be shared by families of processors. Assembly code is almost at the level of machine code, but is more readable and maintainable than raw 0’s and 1’s. It is assembled into machine code.
Assembly Code
Altera DE2 FPGA Hardware
NIOS Processor Image
Machine code is the raw 0’s and 1’s that can be interpreted by the processor in order to execute programs. It is rarely used or modified directly since changes to source code occur at the C Code or Assembly Code levels instead. However, it may be captured as an artifact of the build process for a particular program.
Machine Code
C Code
Compiling
Assembling
Loading
NIOS Processor Hardware
Loading
Flashed
In Lab, we write assembly code for the NIOS processor ( the .s file).

## Slide 39
Assembly code is fairly platform-specific and may be shared by families of processors. Assembly code is almost at the level of machine code, but is more readable and maintainable than raw 0’s and 1’s. It is assembled into machine code.
Assembly Code
Altera DE2 FPGA Hardware
NIOS Processor Image
Machine code is the raw 0’s and 1’s that can be interpreted by the processor in order to execute programs. It is rarely used or modified directly since changes to source code occur at the C Code or Assembly Code levels instead. However, it may be captured as an artifact of the build process for a particular program.
Machine Code
C Code
Compiling
Assembling
Loading
NIOS Processor Hardware
Loading
Flashed
In Lab, we can use the debug monitor to look into memory and see the machine code assembled based on the assembly code.