## Slide 1: ENGR-304-L
Software Lab 06

## Slide 2: Agenda
Attendance
Recap
Polling vs Interrupts
The ISR
Control Registers
Getting Started

## Slide 3: Recap
Bit-Masks
IO Devices
PIO Core & Timer - Altera DE2 IO Devices

## Slide 4: Interrupts
Input devices sometimes use polling
Main routine repeatedly reads/checks input
Do Something
Yes
No
Key
Pushed?
Start

## Slide 5: Interrupts
Input devices sometimes use polling
Main routine repeatedly reads/checks input
Polling can have poor performance
  Poll period fast, wasted checks
  Poll period slow, delayed reaction
Polling multiple inputs can add complexity
Polling can also sometimes be the best solution
Do Something
Yes
No
Key
Pushed?
Start

## Slide 6: Interrupts
Interrupts are an alternative to polling
When input changes, take action immediately
After taking action, resume where interrupted
Do Something
Key
Pushed!
Start

## Slide 7: Interrupts
Interrupts are an alternative to polling
When input changes, take action immediately
After taking action, resume where interrupted
Interrupts require hardware support
Interrupt may alter behavior upon resume
Do Something
Key
Pushed!
Start

## Slide 8: Interrupts
Communication Example
Polling ~ mailbox
Interrupts ~ phone call
Carpooling Example
Polling ~ waiting by the door
Interrupts ~ hearing the doorbell
Useful comparison & justification for each technique:
https://techdifferences.com/difference-between-interrupt-and-polling-in-os.html

## Slide 9: Interrupt Service Routine (ISR)
CPU executing main routine, until interrupt occurs
Main routine is paused, ISR is executed (like a function call)
Main resumes after ISR “returns”
ISR may need to receive data from main routine
ISR may alter data to change behavior in the main routine

## Slide 10: Interrupt Service Routine (ISR)
Main is executing
Device generates interrupt
Main pauses
ISR executes
Main resumes
Main Routine
ISR
Time Start
Time End
Interrupt
Execution Timing Sequence Diagram
Device

## Slide 11: Control Registers
So far… 32 registers

## Slide 12: Control Registers
So far… 32 registers
Now… add 16 more

## Slide 13: NIOS Instructions & Registers
Instructions:
  rdctl
  wrctl
  eret

## Slide 14: NIOS Instructions & Registers
Instructions:
  rdctl = read the value from a control register into a register, similar to mov
  wrctl = write the value from a register into a control register, similar to mov
  eret = return from the ISR

## Slide 15: NIOS Instructions & Registers
Instructions:
  rdctl
  wrctl
  eret
Control Registers:
  ienable
  status
  ipending
  estatus

## Slide 16: NIOS Instructions & Registers
Instructions:
  rdctl
  wrctl
  eret
Control Registers:
  ienable = Allows enabling interrupts by #, each bit gets an interrupt #
  status = Setting the PIE bit enables interrupts for the whole CPU
  ipending = Holds flags for which interrupt(s) are asserted
  estatus = Location to preserve status control register values during ISR

## Slide 17: NIOS Instructions & Registers
Instructions:
  rdctl
  wrctl
  eret
Control Registers:
  ienable
  status
  ipending
  estatus
Registers:
  sp
  et
  ea

## Slide 18: NIOS Instructions & Registers
Instructions:
  rdctl
  wrctl
  eret
Control Registers:
  ienable
  status
  ipending
  estatus
Registers:
  sp = shared by main & ISR, does not need to be protected, used in the same way
  et = temporary register for use during ISR without protection
  ea = like ra but for eret instead of ret

## Slide 19: NIOS Instructions & Registers
Instructions:
  rdctl
  wrctl
  eret
Control Registers:
  ienable
  status Refer to the reference docs!
  ipending
  estatus
Registers:
  sp
  et
  ea

## Slide 20: NIOS Interrupt Execution Sequence
Main is executing
Device generates interrupt
Main pauses
  CPU HW copies PC to EA
  CPU HW copies status to estatus
  CPU HW prevents further interrupts
  CPU HW sets PC to ISR’s location
ISR executes
  Checks interrupt assertions
  Handles interrupts
  Clears interrupt assertions
Main resumes
  Restores estatus to status
  Restores EA to PC
  Re-allows interrupts
Main Routine
ISR
Time Start
Time End
Interrupt
Execution Timing Sequence Diagram
Device

## Slide 21: NIOS Interrupt Setup
Interrupt Enabling
  Enable the device’s interrupts (ex: set mask register)
  Enable the CPU’s interrupts by #
  Clear any left-over interrupt flags
  Enable the CPU’s interrupts globally (status PIE to 1)

## Slide 22: NIOS Interrupt Setup
Interrupt Enabling
  Enable the device’s interrupts (ex: set mask register)
  Enable the CPU’s interrupts by #
  Clear any left-over interrupt flags
  Enable the CPU’s interrupts globally (status PIE to 1)
ISR Creation
  Correct EA if external interrupt (code given)
  Push registers to the stack if needed
  Check each enabled CPU interrupt by #
  Handle asserted interrupts by taking action
  Clear interrupt flags (ex: Timeout bit)
  Pop registers from the stack if needed
  Use eret to resume main routine

## Slide 23: Lab SW06 Tips
Lab SW06 builds on SW05, but use the new template files
Read the template files and comments closely, becomes familiar with them before inserting your own code
Don’t forget to initialize IO devices before use (if needed)
Don’t forget to protect registers on the stack during the ISR (except r0, sp, et, ea)
Refer to “NIOS IO” and “NIOS Interrupts” slide decks for details & examples

## Slide 24: Getting Started
Setup project directory for SW06 on the H: drive
Download SW06 files from Moodle or S: drive
Start following directions in the lab assignment document

## Slide 25: Lab Components
Windows 10 PC
Altera DM
Software (Loading/Debugging)
Altera DE2 Board
Quartus
FGPA
NIOS Processor Image
(Flashed)
Software (Executing)
NIOS Processor Image
NIOS Processor Image
Peripheral Devices
(Ex: switches, buttons, hex displays)
Switches
Timer
7Seg Displays
LEDs
Keys

## Slide 26: PIO Core (Peripheral I/O device/port)

## Slide 27: Interval Timer Core

## Slide 28: Control Registers